## Slide 1: Evaluating ROVIO and OKVIS – Two Visual-Inertial Odometry Implementations
Julian Surber
Semester Thesis
Supervised by Margarita Chli & Lucas Pinto Teixeira

## Slide 2: Intro
One key challenge: Single Robot Localization
Global and Local
Visual-Inertial Odometry
  Complementary Properties
  Lightweight
  Cheap
  Passive, onboard sensors

## Slide 3
Comparing Rovio and Okvis: Working principles, Differences and Accuracy
Visual-Inertial Odometry on non-time-synchronized Hardware?
Outlook
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 4: Overview
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 5: ROVIO – Robust Visual Inertial Odometry Using a Direct EKF-Based Approach
Fast Corner Detector / Multilevel Direct Intensity Patch Features
  Position, Velocity, Attitude, IMU Biases, IMU-Camera Extrinsics, Features (Bearing Vector and Distance to Frame)
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 6: OKVIS – Optimal Keyframe-Based VI SLAM
Harris Corner Detector / BRISK Features
  Nonlinear Optimization of Keyframe Poses, current Frame Poses, Velocity Terms, IMU Biases and Landmark Positions
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 7: Comparison
VI Sensor
Distance 1200 m, handheld, 100 Loops
Dynamics: 2.5 m/s, 3 rad/s
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 8: Global Accuracy – separated axes
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 9: Global Accuracy
Yaw Drift of Rovio 10 times higher over 1000 m
World-z Drift of Rovio 3 times higher over 1000 m
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 10: Local Accuracy
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 11: Results
 | Rovio | Okvis
Global Yaw Error | 45 ° / 1000 m | 4 ° / 1000 m
Global world-z Error | 1 m / 1000 m | 30 cm / 1000 m
Local Translation Error | 2 cm / 1 m | 2 cm / 1 m
Local Orientation Error | 0.6 ° / 1 m | 0.6 ° / 1 m
Processing Time / Frame | 10 ms | Unknown, higher
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 12: Towards non-timesynchronized Hardware 1) Analysis with artificial timedelay
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 13: Towards non-timesynchronized Hardware Real Test
VI Sensor
Bluefox 2.0
Indoor, handheld, 60 m, 3 loops
Slow and Fast Dataset
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 14: Slow Dataset
Dynamics: 1.5 m/s, 1 rad/s
Non-timesynced Hardware is able to track
Visensor performs better
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 15: Fast dataset
Fast, shaky motions
Dynamics: ?, ?
Non-timesynced Hardware diverging
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 16: Fast dataset – Fixed Extrinsics
Fixing the Extrinsics on non-timesynced Hardware increases Rovio performance
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 17: Outlook
Rovio: Include additional Sensorinformation (GPS, Mag)
Rovio: Combine with „Backend“ performing a Global Optimization
Make Okvis running and evaluate
Run Rovio on Embedded system with lower-quality IMU and non-timesynchronized Hardware
Outlook
Rovio and Okvis
Outlook
Time-Synchronization

## Slide 18
Thank you !

## Slide 19: Features / Computational Complexity

## Slide 20: Ev features

## Slide 21: Long Trajectory

## Slide 22
LTE = 2 cm / 1 m (2 %)
LOE = 0.6° / 1 m

## Slide 23
GOE_Yaw = 45 deg / 1000 m
GTE_Z = 1 m / 1000 m (0.1 %)

## Slide 24: Long Trajectory: Summary (create Table!)
Local Accuracy:
  LTE = 2 cm / 1 m (2 %)
  LOE = 0.6° / 1 m
Global Accuracy
  roll and pitch errors bounded
  yaw error = 45 deg / 1000 m
  x and y errors are driven by yaw
  z error = 1 m / 1000 m (0.1 %)
Computational Complexity
  Average Processing Time per Image = 10 ms

## Slide 25: Results
Yaw-Drift of Rovio 10 Times higher than Okvis
Global Translation Error 2 Times higher than Okvis
World-z Error ? Times higher than Okvis
Locally Rovio and Okvis similar (?)

## Slide 26: Short Trajectory

## Slide 27: Evaluation Sheme
Local Accuracy
  Local Translation Error
  Local Orientation Error
Global Accuracy
  Absolute Translation Error
  Absolute Orientation Error
  World-Z Error
  Yaw Error
Computational Complexity
  Processing Time for a new Frame

## Slide 29
LTE = 4 cm / 1 m (4 %) LOE = 0.6° / 1 m

## Slide 31
GOE_Yaw = 1 deg / 50 m
GTE_Z = 5 cm / 50 m (0.1 %)

## Slide 32: ROVIO – Robust Visual Inertial Odometry Using a Direct EKF-Based Approach
State Propagation with IMU (200 Hz)
  Position, Velocity, Attitude, IMU Biases, IMU-Camera Extrinsics, Features (Bearing Vector and Distance to Frame)
Update with Cameraframes (20 Hz)
  Feature Detection with Fast Corner Detector
  Multilevel patch Features
  Direct Intensity Error
„Small“ number of Features

## Slide 33: OKVIS – Optimal Keyframe-Based Visual Inertial SLAM
Nonlinear optimization
  Position, Velocity, Attitude, IMU Biases, Landmarks
Propagation with IMU
Multiscale Harris corner detector
Brisk descriptor aligned with gravity
Marginalization: Keep only several Keyframes and Landmarks
„Large“ number of Features

## Slide 34: Short Trajectory: Summary (create Table!)
Local Accuracy:
  LTE = 4 cm / 1 m (4 %)
  LOE = 0.6° / 1 m
Global Accuracy
  roll and pitch errors bounded
  yaw error = 1 deg / 50 m
  x and y errors are driven by yaw
  z error = 5 cm / 50 m (0.1 %)
Computational Complexity
  Average Processing Time per Image = 10 ms

## Slide 35: Slow Dataset – Global Accuracy
Visensor performs better
New Hardware is able to track

## Slide 36
Yaw Drift
Translational Drift

## Slide 38: Global Error
Thanks to gravity: Roll and Pitch Errors bounded (small)
Yaw Drift
World-X and World-Y Errors driven by Yaw Error
World-Z Drift
Local Errors cancel out  Global Error smaller than integrated local errors

## Slide 40
I
J
B
C
Robot