## Slide 1: Towards generic Visual-Inertial Odometry
Julian Surber
Semester Thesis
Supervised by Margarita Chli & Lucas Pinto Teixeira

## Slide 2
One key challenge: Single Robot Localization
Global and Local
Visual-Inertial Odometry
  Complementary Properties
  Lightweight
  Passive
  Onboard

## Slide 3
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 4: Overview
Outlook
Time-Synchronization
ROVIO and OKVIS
2 [Leutenegger et al., IJRR, 2015]
1
2
1 [Blösch et al., IROS, 2015]
Notes: Filtering-based: 2 steps ...
The information of a past observation is transferred into the Current Frame via the Prior Belief of the Filter.
But a Past Estimate will never be corrected based on the current observation.
Keyframe-based: nonlinear optimization based on a large number of landmark observations taken from a SET of past keyframes and the current frame.
Like that poses of the past are corrected based on the current observation.
ROVIO and OKVIS

## Slide 5: ROVIO – Robust Visual Inertial Odometry Using a Direct EKF-Based Approach
Fast Corner Detector / Multilevel Direct Intensity Patch Features
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 6: OKVIS – Optimal Keyframe-Based VI SLAM
Harris Corner Detector / BRISK Descriptor
  Nonlinear Optimization
Outlook
Time-Synchronization
ROVIO and OKVIS
[Leutenegger et al.,
IJRR, 2015]

## Slide 7: Comparison
VI Sensor
Distance 1200 m, handheld, 100 Loops
Dynamics: 2 m/s, 3 rad/s
Start /
Endpoint
Outlook
Time-Synchronization
ROVIO and OKVIS
[Nikolic et al., ICRA, 2014]
Notes: I want to compare the two presented algorithms on a dataset Simon Lynen collected to evaluate OKVIS.
long trajectory captured indoors, 100 handheld loops
It is not clear out of this graph, but what happened was

## Slide 8: Global Accuracy
Outlook
Time-Synchronization
ROVIO and OKVIS
Notes: If you look at the orientation error at the axes separately, the roll and pitch errors are bounded and below 1 degree for both algorithms over the whole sequence. Thanks to the IMU the gravity vector is observable and therefore errors around axes lying in the horizontal plane are bounded.
The major contribution to the absolute orientation error is coming from the yaw error – the rotation around the world-z axis.

## Slide 9: Local Accuracy
Outlook
Time-Synchronization
ROVIO and OKVIS
Notes: In addition to the Global Accuracy it is of great interest how well tracking is working on short distances.
The relative translation error compares the true and estimated Travelled Distance between two frames.

## Slide 10: Results
Outlook
Time-Synchronization
ROVIO and OKVIS
Absolute Error | 
ROVIO | OKVIS
2.5 m / 1000 m | 1 m / 1000 m
45 ° / 1000 m | 4 ° / 1000 m
Relative Error | 
ROVIO | OKVIS
2 cm / 1 m | 2 cm / 1 m
0.6 ° / 1 m | 0.6 ° / 1 m
Computational Complexity | 
ROVIO | OKVIS
10 ms / Frame | unknown, higher
Notes: Gap in Global Accuracy
Similar Local Accuracy
Regarding Computational Complexity ROVIO is
Beside of these results there is an additional “soft” argument for Rovio: It is working robustly for many people in here – live with the visensor, in simulation and on other different datasets I was working on.

## Slide 11: Towards non-timesynchronized Hardware
Outlook
Time-Synchronization
ROVIO and OKVIS
1) Analysis with artificial bias on IMU timestamp
Notes: Go over to the second part, where I takle the question if Visual-Inertial Odometry is able to work with data from non-timesynchronized Hardware.
The VI SENSOR is hardwarewise timesynchronized, which means that the IMU is triggering the image capture and the sensor signals arrive perfectly time-aligned.
As a first analysis I took data from the visensor and added an artifical bias on the IMU timestamp
1) For this data: ROVIO is surprisingly robust untill 50 ms, DIVERGING at 100ms
2) A second result ...
Normally Rovio is estimating the camera-IMU extrinsics constantly

## Slide 12: Towards non-timesynchronized Hardware 2) Real Test
VI Sensor
Bluefox 2.0
Indoor, handheld, 60 m, 3 loops
Slow and Fast Dataset
Outlook
Time-Synchronization
ROVIO and OKVIS
Notes: This analysis encouraged us ...

## Slide 13: Slow Dataset
Dynamics: 1.5 m/s, 1 rad/s
Non-timesynchronized Hardware is able to track
Visensor performs better
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 14: Fast dataset
Fast, shaky motions
Dynamics: 2.5 m/s, 5 rad/s
Non-timesynchronized Hardware diverging
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 15: Fast dataset – Fixed Extrinsics
Fixing the Extrinsics can increases Rovio performance on non-timesynced Hardware
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 16: Outlook
Rovio: Combine with „Backend“ performing a Global Optimization
Rovio: Include additional Sensorinformation (GPS, Magnetometer)
Run Rovio on embedded system with lower-quality IMU and non-timesynchronized Hardware
Run and evaluate Okvis
Outlook
ROVIO and OKVIS
Outlook
Time-Synchronization

## Slide 17
Thank you !

## Slide 18: Global Accuracy – separated axes
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 19: Global Accuracy
Yaw Drift of Rovio 10 times higher over 1000 m
World-z Drift of Rovio 3 times higher over 1000 m
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 22: Global Accuracy – Euroc Data

## Slide 23: Global Accuracy – Euroc Data
AOE_Yaw = 1 deg / 50 m
ATE_Z = 5 cm / 50 m (0.1 %)

## Slide 24: Local Accuracy – Euroc Data
RTE = 4 cm / 1 m (4 %)
ROE = 0.6° / 1 m

## Slide 25: Slow Dataset
Dynamics: 1.5 m/s, 1 rad/s
Non-timesynchronized Hardware is able to track
Visensor performs better
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 26: Fast dataset
Fast, shaky motions
Dynamics: 2.5 m/s, 5 rad/s
Non-timesynchronized Hardware diverging
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 27: Fast dataset – Fixed Extrinsics
Fixing the Extrinsics on non-timesynced Hardware increases Rovio performance
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 28: Results – Euroc Data
 | Rovio | Okvis
Absolute Translation Error | 5 cm / 50 m | -
Absolute Orientation Error | 45 ° / 50 m | -
Absolute Yaw Error | 1 ° / 50 m | -
Absolute world-z Error | 5 cm / 50 m | -
Relative Translation Error | 4 cm / 1 m | -
Relative Orientation Error | 0.6 ° / 1 m | -
Processing Time / Frame | 10 ms | unknown, higher
Outlook
Time-Synchronization
Rovio and Okvis

## Slide 29: Computational Complexity / Features – Euroc Data