## Slide 1: Towards generic Visual-Inertial Odometry
Julian Surber
Semester Thesis
Supervised by Margarita Chli & Lucas Pinto Teixeira

## Slide 2
One key challenge: Single Robot Localization
Global and Local
Visual-Inertial Odometry
  Complementary Properties
  Lightweight
  Passive
  Onboard

## Slide 3
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 4: Overview
Outlook
Time-Synchronization
ROVIO and OKVIS
2 [Leutenegger et al., IJRR, 2015]
1
2
1 [Blösch et al., IROS, 2015]
Notes: Filtering-based: 2 steps ...
The information of a past observation is transferred into the Current Frame via the Prior Belief of the Filter.
But a Past Estimate will never be corrected based on the current observation.
Keyframe-based: nonlinear optimization based on a large number of landmark observations taken from a SET of past keyframes and the current frame.
Like that poses of the past are corrected based on the current observation.
ROVIO and OKVIS

## Slide 5: ROVIO – Robust Visual Inertial Odometry Using a Direct EKF-Based Approach
Fast Corner Detector / Multilevel Direct Intensity Patch Features
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 6: OKVIS – Optimal Keyframe-Based VI SLAM
Harris Corner Detector / BRISK Descriptor
  Nonlinear Optimization
Outlook
Time-Synchronization
ROVIO and OKVIS
[Leutenegger et al.,
IJRR, 2015]

## Slide 7: Comparison
VI Sensor
Distance 1200 m, handheld, 100 Loops
Dynamics: 2 m/s, 3 rad/s
Start /
Endpoint
Outlook
Time-Synchronization
ROVIO and OKVIS
[Nikolic et al., ICRA, 2014]
Notes: I want to compare the two presented algorithms on a dataset Simon Lynen collected to evaluate OKVIS.
long trajectory captured indoors, 100 handheld loops
It is not clear out of this graph, but what happened was

## Slide 8: Global Accuracy
Outlook
Time-Synchronization
ROVIO and OKVIS
Notes: If you look at the orientation error at the axes separately, the roll and pitch errors are bounded and below 1 degree for both algorithms over the whole sequence. Thanks to the IMU the gravity vector is observable and therefore errors around axes lying in the horizontal plane are bounded.
The major contribution to the absolute orientation error is coming from the yaw error – the rotation around the world-z axis.

## Slide 9: Local Accuracy
Outlook
Time-Synchronization
ROVIO and OKVIS
Notes: In addition to the Global Accuracy it is of great interest how well tracking is working on short distances.
The relative translation error compares the true and estimated Travelled Distance between two frames.
The relative orientation error compares the true change in attitude with the estimated change in attitude between two frames.

## Slide 10: Results
Outlook
Time-Synchronization
ROVIO and OKVIS
Absolute Error | 
ROVIO | OKVIS
2.5 m / 1000 m | 1 m / 1000 m
45 ° / 1000 m | 4 ° / 1000 m
Relative Error | 
ROVIO | OKVIS
2 cm / 1 m | 2 cm / 1 m
0.6 ° / 1 m | 0.6 ° / 1 m
Computational Complexity | 
ROVIO | OKVIS
10 ms / Frame | unknown, higher
Notes: Gap in Global Accuracy
Similar Local Accuracy
Regarding Computational Complexity ROVIO is
Beside of these results there is an additional “soft” argument for Rovio: It is working robustly for many people in here – live with the visensor, in simulation and on other different datasets I was working on.

## Slide 11: Towards non-timesynchronized Hardware
Outlook
Time-Synchronization
ROVIO and OKVIS
Notes: Go over to the second part, where I takle the question if Visual-Inertial Odometry is able to work with data from non-timesynchronized Hardware.
The VI SENSOR is hardwarewise timesynchronized, which means that the IMU is triggering the image capture and the sensor signals arrive perfectly time-aligned.
To see if Rovio can work with a non timesynchronized Sensorsystem we attached ...

## Slide 12: Slow Dataset
Dynamics: 1.5 m/s, 1 rad/s
Non-timesynchronized Hardware is able to track
Visensor performs better
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 13: Fast dataset
Fast, shaky motions
Dynamics: 2.5 m/s, 5 rad/s
Non-timesynchronized Hardware diverging
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 14: Fast dataset – Fixed Extrinsics
Fixing the Extrinsics can increases Rovio performance on non-timesynced Hardware
Outlook
Time-Synchronization
ROVIO and OKVIS

## Slide 15: Outlook
Rovio: Combine with a Secondary Module performing a Global Optimization
Run Rovio on embedded system with lower-quality IMU and non-timesynchronized Hardware
Run and evaluate Okvis
Outlook
ROVIO and OKVIS
Outlook
Time-Synchronization
Notes: Summerizing the presented work we saw, that
1) Rovio and Okvis are both promising Visual-Inertial Odometry Implementations
2) Rovio is prone to drift – especially in Yaw
3) Rovio and Okvis showed similar and good performance regarding local accuracy
4) Rovio is principally able to run on a non-hardware-timesynchronized Sensorsystem
This brings me to the outlook after this Semesterthesis.

## Slide 16
Thank you !

## Slide 17: Global Accuracy – separated axes – IJRR

## Slide 18: Slow Dataset

## Slide 19: Fast dataset – Fixed Extrinsics

## Slide 20: Global Accuracy ROVIO – Euroc Data

## Slide 21: Global Accuracy ROVIO – Euroc Data
AOE_Yaw = 1 deg / 50 m
ATE_Z = 5 cm / 50 m (0.1 %)

## Slide 22: Local Accuracy ROVIO – Euroc Data
RTE = 4 cm / 1 m (4 %)
ROE = 0.6° / 1 m

## Slide 23: Computational Complexity / Features – Euroc Data