## Slide 1: Visual-Inertial Odometry: Evaluating ROVIO and OKVIS
Julian Surber
Semester Thesis
Supervised by Margarita Chli & Lucas Pinto Teixeira

## Slide 2: Intro
One key challenge: Single Robot Localization
Global and Local
Visual-Inertial Odometry

## Slide 3: State of the Art

## Slide 4: ROVIO – Robust Visual Inertial Odometry Using a Direct EKF-Based Approach
State Propagation with IMU (200 Hz)
  Position, Velocity, Attitude, IMU Biases, IMU-Camera Extrinsics, Features (Bearing Vector and Distance to Frame)
Update with Cameraframes (20 Hz)
  Feature Detection with Fast Corner Detector
  Multilevel patch Features
  Direct Intensity Error
„Small“ number of Features

## Slide 5: ROVIO – Robust Visual Inertial Odometry Using a Direct EKF-Based Approach

## Slide 6: OKVIS – Optimal Keyframe-Based Visual Inertial SLAM
Nonlinear optimization
  Position, Velocity, Attitude, IMU Biases, Landmarks
Propagation with IMU
Multiscale Harris corner detector
Brisk descriptor aligned with gravity
Marginalization: Keep only several Keyframes and Landmarks
„Large“ number of Features

## Slide 7: OKVIS – Optimal Keyframe-Based Visual Inertial SLAM

## Slide 8: Comparison - Global Accuracy

## Slide 9: Global Accuracy – separated axes

## Slide 10: Global Accuracy – yaw and world-z
Rovio:
Okvis:

## Slide 11: Local Accuracy
Rovio:
Okvis:

## Slide 12: Results
 | Rovio | Okvis
Global Translation Error | 2.5 m / 1000 m | 1 m / 1000 m
Global Orientation Error | 45 ° / 1000 m | 4 ° / 1000 m
Global Yaw Error | 45 ° / 1000 m | 
Global world-z Error | 1 m / 1000 m | 
Local Translation Error | 2 cm / 1 m | 
Local Orientation Error | 0.6 ° / 1 m | 
Processing Time / Frame | 10 ms | unknown

## Slide 13: VI Sensor
High-quality global-shutter Cameras
High-quality IMU
Hardware time-synchronized

## Slide 14: Towards non-timesynchronized Hardware
Artificial Bias on IMU-Timestamp
Real Test with VI-Sensor and Bluefox2 Camera

## Slide 15: Slow Dataset
Dynamics: 1.5 m/s, 1 rad/s
Distance: 50 m, 3 loops
Visensor performs better
Non-timesynced Hardware is able to track

## Slide 16: Fast dataset
Dynamics: ?, ?
Distance: 60 m
Non-timesynced Hardware diverging

## Slide 17: Fast dataset – Fixed Extrinsics
Fixing the Extrinsics on non-timesynced Hardware increases Rovio performance

## Slide 18: Outlook
Rovio: Include additional Sensorinformation (GPS, Mag)
Rovio: Combine with „Backend“ performing a Global Optimization
Make Okvis running and evaluate
Run Rovio on Embedded system with lower-quality IMU and non-timesynchronized Hardware

## Slide 19
Thank you !

## Slide 20: Features / Computational Complexity

## Slide 21: Ev features

## Slide 22: Long Trajectory

## Slide 23
LTE = 2 cm / 1 m (2 %)
LOE = 0.6° / 1 m

## Slide 24
GOE_Yaw = 45 deg / 1000 m
GTE_Z = 1 m / 1000 m (0.1 %)

## Slide 25: Long Trajectory: Summary (create Table!)
Local Accuracy:
  LTE = 2 cm / 1 m (2 %)
  LOE = 0.6° / 1 m
Global Accuracy
  roll and pitch errors bounded
  yaw error = 45 deg / 1000 m
  x and y errors are driven by yaw
  z error = 1 m / 1000 m (0.1 %)
Computational Complexity
  Average Processing Time per Image = 10 ms

## Slide 26: Results
Yaw-Drift of Rovio 10 Times higher than Okvis
Global Translation Error 2 Times higher than Okvis
World-z Error ? Times higher than Okvis
Locally Rovio and Okvis similar (?)

## Slide 27: Short Trajectory

## Slide 28: Evaluation Sheme
Local Accuracy
  Local Translation Error
  Local Orientation Error
Global Accuracy
  Absolute Translation Error
  Absolute Orientation Error
  World-Z Error
  Yaw Error
Computational Complexity
  Processing Time for a new Frame

## Slide 30
LTE = 4 cm / 1 m (4 %) LOE = 0.6° / 1 m

## Slide 32
GOE_Yaw = 1 deg / 50 m
GTE_Z = 5 cm / 50 m (0.1 %)

## Slide 33: Short Trajectory: Summary (create Table!)
Local Accuracy:
  LTE = 4 cm / 1 m (4 %)
  LOE = 0.6° / 1 m
Global Accuracy
  roll and pitch errors bounded
  yaw error = 1 deg / 50 m
  x and y errors are driven by yaw
  z error = 5 cm / 50 m (0.1 %)
Computational Complexity
  Average Processing Time per Image = 10 ms

## Slide 34: Slow Dataset – Global Accuracy
Visensor performs better
New Hardware is able to track

## Slide 35
Yaw Drift
Translational Drift

## Slide 37: Global Error
Thanks to gravity: Roll and Pitch Errors bounded (small)
Yaw Drift
World-X and World-Y Errors driven by Yaw Error
World-Z Drift
Local Errors cancel out  Global Error smaller than integrated local errors

## Slide 39
I
J
B
C
Robot